ZONE LIST

This document describes the Zone List for the residence units in Piyalepaşa İstanbul Project.

The zone list describes general design and application principles as well as the general rules of the system and materials to be used. It does not constitute the basis for the brands, designs, colors, and models with regard to the types of architectural materials, kitchen and bathroom cabinets, joinery and doors, nor to any other fabrications done with any other materials. Piyalepaşa Gayrimenkul Geliştirme Yatırımı Ticaret A.Ş. reserves the right to make any changes to the zone list if required technically or administratively.

04.2004

1. CONSTRUCTION

Load Bearing structure:

- The load bearing structure will be a conventional reinforced concrete shear wall and column system on a spread foundation. TSE-approved plant mixed concrete and ribbed reinforcing concrete steel will be used in Construction of reinforced concrete load bearing structure.

- Soil investigations reports  were prepared through boring studies..

- If it is find essential by the Geotechnical Advisor, several ground improvement techniques, compatible to all technical specifications and standards, will be employed underneath the foundations of the buildings. (jet – grout, bored pile system etc.)

Facade:

A thermal insulation jacketing system and/or coating material will be used on all exterior walls in accordance with the project.

Interior walls:

Interior walls will consist of hollow bricks, aerated concrete covered with gypsum plaster or plasterboard, or other similar materials to be determined compatible to the architectural project.

Roof:

All buildings will have a terraced roof system according to the project and its terms and conditions. Thermal and water insulation system will be employed on the terrace roofs compatible to the project and its terms and conditions.

Window Frames:

Window frames will be manufactured from TSE-certified PVC profiles. Their design will ensure taking advantage of maximum sunlight. "Thermal-insulated" glass from "Isıcam" or an equivalent brand will be used for windows.

Heating, water, and sound insulation:

- The building foundations and the exterior walls of basement floors will be waterproofed in accordance with the project.

- Based on the heat loss and gain value standards in calculations and reports of technical specs, at any necessary locations, thermal insulation will be applied on the ground and interior wall manufacturings.

- Thermal insulation and waterproofing will be employed on the terraced roofs of all buildings in accordance with the projects.

- Waterproofing will be applied in wet areas.

- Sound insulation will be applied, in accordance with the regulations, in all places that house the water booster system and water tanks.

- A glass fiber-reinforced sound insulation blanket will be used to achieve impact sound insulation inside the apartments, except in wet areas..

- A thermal insulation sheathing system and/or coating material will be used on all exterior walls in accordance with the project.

- Precautions in line with the directives and terms and conditions will be taken where necessary, as indicated in calculations of heat loss and gains in reports for each detached unit and between each apartment buildings.

- Noise insulation will be done between each detached unit based on calculations and noise measurements in reports.

2. APARTMENT INTERIORS

Doors:

Unit entrance	: Steel doors that match the project and design of units will be installed.

Doors within the unit	: Wooden vaulted, lathed, and coated doors that match the design will be installed. Type of coating will be determined according to the principles of the project's architectural design.

Foyer and Hallway:

Floor covering:	1+0 (studio) and 1+1 apartments will have laminate / laminate parquet or ceramic; all other apartments will have ceramic.

#### Wall covering:	 Water-based paint will be applied on gypsum plaster on the walls.

Ceiling covering:	 Water-based paint will be applied on gypsum plaster on the ceilings.

Cabinets	: All apartments will have coat closets with doors in the foyer.

Living Room:

Floor Covering:	 First-class laminate or laminate parquet will be installed.

##### Wall covering:	 Water-based paint will be applied on gypsum plaster on the walls.

### Ceiling covering	: Water-based paint will be applied on gypsum plaster on the ceilings.

Bedrooms:

Floor Covering:	 First-class laminate or laminate parquet will be installed.

##### Wall covering:	 Water-based paint will be applied on gypsum plaster on the walls.

### Ceiling covering	: Water-based paint will be applied on gypsum plaster on the ceilings.

Kitchen:

#### Floor Covering:	 Laminate or laminate parquet will be installed in all apartments with open-plan kitchens while all the other apartment types will have first-class ceramic.

###### Wall Covering:	 Water-based paint will be applied on gypsum plaster on the walls while the backsplash will be covered with ceramic.

###### Ceiling covering:	 Water-based paint will be applied on gypsum plaster on the ceilings. Plasterboard suspended ceiling will be installed as necessary.

Cabinets:	 Cabinets will be built from melamine-covered particle board in line with the project. Side doors will be covered with PVC membrane or laminate over MDF. Glass doors will be built on an aluminum frame. Countertops will be laminate.

Lighting Fixtures:	 First-class locally-manufactured lighting fixtures will be used.

Sink:	 Stainless steel sink with 1 or 1.5 holes and a draining board.

Kitchen appliances:	 All apartments will be delivered with an energy-efficient built-in dishwasher, stovetop, oven, and range hood.

Bathroom:

#### Floor Covering	: First-class locally-manufactured ceramic will be used.

Wall Covering	: First-class domestically-produced tiles will be used.

Ceiling Covering:	 Paint will be applied on plaster.

Bathroom Cabinet:	 Cabinets will be covered with PVC membrane or laminate over MDF

and will have mirrors and lighting.

Lighting Fixtures:		 First-class lighting fixtures will be used.

Bathroom Fixtures:		 First-class bathroom fixtures will be used.

Bathtub and Shower Cabin: First-class bathtub and/or shower cabins will be used. Shower cabins with tempered glass will be installed.

Balconies:

Floor Covering: First-class domestic ceramic.

##### Wall Covering:	 Silicon-based or other external surface paint

##### Ceiling Covering:	 Silicon-based or other external surface paint

##### Railing:		 Tempered laminated glass aluminum or iron sheet railing

##### will be installed.

3. ELECTRICAL SYSTEM

Low Voltage Electrical Distribution Installation:

- Grounding will be installed in all buildings.

- A convenient lightning protection system will be installed in the buildings in compliance with the projects and regulations.

- Panels will have a residual current circuit breaker to protect against accidents.

- A transformer substation will be built to provide energy to the buildings.

- All power outlets inside the apartment will have a "child safety" feature.

- Telephone and television outlets will be installed in the living room and every bedroom in all apartments.

- A sufficient number of electrical outlets will be installed in kitchens, bathrooms, and en-suite bathrooms.

- Foyers, hallways, kitchens, bathrooms, and balconies will all have top-notch domestically-produced lighting fixtures.

- Battery-charged “Emergency Lighting” (at least one) will be provided as necessary in the hallways inside the apartments as well as in the staircases and hallways of fire escapes.

- Energy-efficient lighting fixtures will be used.

TV System:

A “Headent” system will be installed for satellite television broadcasts. Each apartment will be provided with 40 channels of analog broadcast, Digiturk, D-Smart, and a 20-package digital broadcast. Apartment residents will be able to watch analog and digital broadcasts directly through the decoder (which can be connected to any television outlet) by subscribing to Digiturk or D-Smart. The number of digital channels may vary depending on the package selected. The system will allow for obtaining additional packages from new or encrypted channels.

Telephone and Internet System:

Each room will feature telephone and internet connection outlets that will contain both the telephone and internet lines.

Back-up Energy System:

In the event of power outages, all homes, outdoor lighting, building entrances, water booster systems and fire tanks, elevators, intercoms, fire alarm systems and switchboards, staircases, floor halls, central heaters, hot water systems, and parking garages shall be provided electricity through the installed generators.

Intercom System:

- A digital intercom system with color images will be installed in all apartments. The system will control the front entrance of the building and will allow for dialogue between the apartment and the door.

- It will be possible to call security from all of apartments and elevators and, if necessary, security will be able call the apartments.

- A doorbell panel will be placed at the entrance of the buildings. This panel will allow calls to be made from the building entrances. In addition, apartment owners will be able to open the building entrance door with a password allowing them to enter without having to use a key.

Elevators:

An adequate number of elevators that comply with the project and TSE and CE standards will be supplied and installed according to the specifications. They will have air conditioning and security alarms and will allow for communication with security in case of emergency.

4. SANITARY SYSTEM

Potable Water System:

Tap water will be obtained from the city's main distribution network. Tap water will be delivered from the tanks through the water booster system then moved through the cold-water meter via the entrance of the apartment building to be sent to the housing unit. Cold water usage will be measured and billed separately each month for each detached unit.

Cold water will be delivered through galvanized pipes for the main pipelines and PPRC Type 3 pipes inside the apartments.

Waste Water System:

TSE-certified PVC-based pipes and fittings will be used inside the main pipeline and for the basement floor collection areas to be connected to the main sewage system.

Hot Water System:

Homes will be provided with hot water 24 hours a day through a centralized boiler system.

Each detached unit’s hot water usage will be measured and billed separately every month through the hot water meter with the “M-Bus” interface, which will be placed on the water installations for each unit.

Potable Water Storage:

A back-up water tank will be built at the complex.

5. HEATING SYSTEM

Each apartment will be heated through the central heating system with hot water boilers working on natural gas. Electromechanical or Ultrasonic heat flow meters (calorimeters) equipped with the "M-Bus" operation interface placed at the installation shafts built for each detached unit will be used to measure energy consumption and to bill each unit based on individual usage as well the unit's share of usage in common areas.

Underfloor heating will be used to heat the apartments.

6. AIR CONDITIONING

Class “A” energy efficiency split air conditioners, consisting of one external unit and two internal units, will be installed in 2+1, 3+1, and 4+1 apartments. The split air conditioners in 1+0 (studio) and 1+1 apartments will consist of one external and one internal unit.

7. FIRE EQUIPMENT:

- Fire alarm and extinguishing systems will be installed in all common areas according to the Turkish Regulation on Fire Protection.

- Fire extinguisher cabinets, fire alarm buttons, and fire detectors will be installed on floor halls.

- At building entrances, social facilities within the complex, and centrally heated areas, the natural gas installation will have a solenoid valve that automatically cuts off the gas during earthquakes and upon gas detection.

- Optical smoke detectors and heat detectors will be installed in all apartments and kitchens as stipulated by the project.

- A fire alarm system in parking garages, carbon monoxide (CO) detectors at places shown in the plans, fire alarms, fire extinguisher cabinets, and sprinkler systems will be installed.

- An “exit” sign will be placed to show the emergency escape routes on all fire escape doors, elevator halls, and common and general areas.

- “Emergency Lighting” will be designed to allow illumination without interruption during a power outage.

- Each staircase and fire elevator will be centrally pressurized to flush out smoke from each floor hall.

8. CAR PARKING

- A number of indoor parking garage spaces will be allocated to each unit, determined according to the  Management Plan.

- Pedestrian and disabled access will be provided to all apartments through elevators and/or stairs directly from garages.

- A mechanical exhaust ventilation and smoke removal system is in place in the parking garage. A gas (carbon monoxide) detection and alarm system will be installed in certain parts of the parking garage.

9. STORAGE AREAS FOR DETACHED UNITS

A storage area will be allocated at the basement for each apartment according to the architectural plan.

10. LANDSCAPING AND OUTDOOR SET-UP

- Non-residential areas of the building will be planned as recreational, garden, and social facility spaces.

- General landscaping will be done using an automatic drip irrigation system according to the architectural plan.

- Lighting of the green areas and pedestrian crossings, as well as the landscaping and design of shared gardens within the complex, will be done according to the project and management plan.

- Infrastructure for vehicles and pedestrians, sewage, water, and drainage systems will be constructed.

11. COMMON AREAS OF THE BUILDING

- Marble, artificial marble, and/or granite will be used on staircases, main entrances, and outer staircases.

- Entrance halls of the buildings will have personal mail boxes with locks for each apartment.